## Slide 1
Wildfire activity is increasing across Canada, with a statistically significant increase in burned area nationally and in British Columbia, Alberta, Saskatchewan, and the Northwest Territories
Long-range smoke transport leads to elevated PM2.5 levels that pose serious respiratory and cardiovascular health risks.
Currently, major cities often receive little advance warning before smoke arrives.
This project developed the C.L.E.A.R early-warning system to predict wildfire-related PM2.5 spikes in Toronto, Edmonton, Montreal, and Vancouver by detecting smoke at distant air-quality monitoring stations (100-600+ km away), providing 6-48+ hours of advance warning (depending on station distance)
This system could allow schools, hospitals, and municipalities to act before air quality deteriorates
Purpose
Can hourly PM2.5 measurements at distant air-quality stations accurately predict PM2.5 levels in major Canadian cities with enough lead time to issue early warnings for wildfire smoke events?
Figure 3: Statistically significant increases in burn area were identified, supporting the need for an early-warning PM2.5 alert system. Data source: National Forestry Database, Natural Resources Canada (2025). Regression analysis and visualization generated with Claude AI (Anthropic).
The National Air Pollution Surveillance (NAPS) Program is Canada’s national air-quality monitoring network, operated by Environment and Climate Change Canada
Measures: PM2.5, Ozone (O3), nitrogen dioxide (NO2), sulfur dioxide (SO2).
84% of stations are located in BC, AB, ON, and QC, providing dense regional coverage.
High station density allows wildfire smoke to be detected hundreds of kilometres upstream before it reaches major cities
Vancouver, Edmonton, Toronto, and Montreal were selected because their surrounding monitoring networks provide sufficient spatial coverage to enable advanced smoke detection and early warning
Figure 1: National Air Pollution Surveillance (NAPS) Program. Visualization generated using Claude AI (Anthropic).
Figure 4: Scatter plot shows the relationship between station distance from the target city and PM2.5 correlation strength (R). Correlation decreases with distance but remains sufficient for early warning. Data source: NAPS Program, Environment and Climate Change Canada. Regression analysis and visualization generated with Claude AI (Anthropic).
Figure 5: Air monitoring stations surrounding each city at varying distances provide 360° early-warning coverage, detecting smoke regardless of wind directions. Map generated with Claude AI (Anthropic).
Alert Level | PM2.5 Level | Public Health Action Plan
Low | < 20 ug/m3 | No precautions needed.
Moderate | 21-60 ug/m3 | Sensitive groups (children/elderly) avoid strenuous activities.
High | 61-80 ug/m3 | Everyone should reduce physical exertion. N95 or KN95 mask. Keep doors and windows closed. HVAC to recirculate. Run HEPA filter.
Very High | 81-120 ug/m3 | Avoid all outdoor activity. Keep hydrated.
Extreme | > 120 ug/m3 | Halt indoor pollution. No frying or sauteing. No vacuuming. No candles. No wood-burning stoves.
Table 1: The early warning system alert scale and recommendations. Table created with PowerPoint.
Integrate satellite smoke detection data for longer-range warning.
Expand to additional Canadian cities.
Test system performance during actual smoke events.
Advocate for expanded NAPS coverage in Saskatchewan, Manitoba and the Northwest Territories.
Created a C.L.E.A.R. APP for incorporating real-time wind direction and speed data to improve prediction accuracy.
Correlation Analysis
  Statistical correlations were calculated between target cities and distant monitoring stations during wildfire season (May-September) to isolate wildfire smoke and exclude non-wildfire PM2.5 sources
Regression Model
  Target city PM2.5 = Slope x Station PM2.5 + intercept
Why hourly data?
  Wildfire smoke travels 30-50 km/hr → early detection requires hourly PM2.5
  Lower correlations reflect short-term variability, not reduced predictive value
Station selection criteria
  Stations were included only if ALL criteria were met:
    Correlation (R) ≥ 0.30
    Significance (P) < 0.001
    Sample Size (N) ≥ 100
Early Warning System
  Identified 218 monitoring stations providing 6-48+ hours of advance warning
  Alert thresholds calculated using the WHO PM2.5 health guidelines
  Built a 360° early warning network around each city
  Validated using historical wildfire events
Computational Analysis
  Large-scale data analysis of 36+ million hourly PM2.5 observations was performed using Claude AI (Anthropic)
NAPS (Canada) and U.S. EPA AQS/AirNow, 2003-2023
Study period:
  2003: start of modern PM2.5 monitoring
  2023: most recent validated data (Environment and Climate Change Canada)
City | True Positive | False Negative | True Negative | False Positive | Detection | False Alarm | Status
Vancouver | 14 | 0 | 10 | 0 | 100% | 0% | Perfect
Edmonton | 9 | 1 | 5 | 0 | 90% | 0% | 1 Failure
Toronto | 10 | 0 | 10 | 0 | 100% | 0% | Perfect
Montreal | 14 | 0 | 10 | 0 | 100% | 0% | Perfect
Total | 47 | 1 | 35 | 0 | 97.9% | 0% | 83 events
Anthropic. (2026). Claude AI (Version 3.5 Sonnet) [Large language model]. https://claude.ai
Cruz, M. G., Alexander, M. E., & Sullivan, A. L. (2019). Toward a model for estimating fire spread rate in seasonally dormant grasslands and shrublands. Annals of Forest Science, 76(2), Article 44. https://doi.org/10.1007/s13595-019-0829-8
Environment and Climate Change Canada. (n.d.-b). National Air Pollution Surveillance (NAPS) Program. Government of Canada. https://www.canada.ca/en/environment-climatechange/services/air-pollution/monitoring-networks-data/national-air-pollutionprogram.html
Environment and Climate Change Canada. (n.d.-c). PM2.5 data portal: National Air Pollution Surveillance (NAPS) Program. Government of Canada. https://datadonnees.az.ec.gc.ca/data/air/monitor/national-air-pollution-surveillance-napsprogram/Data-Donnees?lang=en
Environment and Climate Change Canada. (n.d.-d). Representative Concentration Pathways. Government of Canada. https://climate-scenarios.canada.ca/?page=scen-rcp
IQAir. (2021). WHO air quality guidelines. https://www.iqair.com/ca/newsroom/2021-who-airquality-Guidelines
National Forestry Database of Canada. (n.d.). Forest fires. Canadian Council of Forest Ministers. http://nfdp.ccfm.org/en/data/fires.php#tab323
United States Environmental Protection Agency. (n.d.). Air quality data: Download daily data. https://www.epa.gov/outdoor-air-quality-data/download-daily-data
Notes on AI Tool Usage
Claude AI (Anthropic, 2026) was used for the following components of this research project:
Large-scale data processing of 36+ million hourly PM₂.₅ observations from the NAPS and US EPA databases
Linear regression analysis for 445 monitoring stations across Canada and the United States
Generation of data visualizations, including maps, scatter plots, and trend analyses
Cross-platform validation was performed using four independent AI platforms (Claude, ChatGPT, Gemini, and Jules) to confirm reproducibility of statistical results
Table 2: Confusion matrix results for the PM2.5 Early Warning System, validated using 83 historical wildfire smoke events (2003-2023). Table created with PowerPoint.
An “event” is defined as a city-level smoke impact; a single wildfire may affect multiple cities.
Research Question
Data Sources
Methods
National Air Pollution Surveillance (NAPS)
Forest Fire Burn Area Analysis
The C.L.E.A.R System: The NAPS Early Warning Station Network
AI Platform Validation
How the C.L.E.A.R. Early Warning System Works: A Real Example
Historical Validation
2024 Data Validation
Real-Time Automated C.L.E.A.R. Alert System
Conclusion
Data Sources and Acknowledgements
System Flowchart
Figure 2: Correlation of PM2.5 Concentrations with Canadian AQHI Risk Levels. This chart synthesizes the PM2.5 concentration breakpoints used in AQHI-Plus wildfire amendment (Yao et al., 2019) with national safety benchmarks (CCME, 2023) and global health guidelines (WHO, 2021). Risk categories and indoor recommendations are derived from Health Canada’s residential air quality framework. The visualization was created using Adobe Photoshop.
Figure 9: Example of C.L.E.A.R. early warning system. Visualization created with PowerPoint and Adobe Photoshop.
Future Work
Near-Perfect Validation
47 of 48 smoke events (97.9%)
successfully detected
Zero False Alarms
All 35 non-impact forest fires
received NO warning
Edmonton Failure Analysis
One event (449 ug/m3) missed due to gap in NNW monitoring coverage
This failure demonstrates that network gaps, not model limitations, are the primary risk
Recommend additional monitoring stations:
  Jarvie (107 km NNW): Tier 2 coverage
  Athabasca (145 km N): Tier 2 northern coverage
  Whitecourt (175 km WNW): Tier 2 improved western boreal coverage
  Slave Lake (250 km N): Tier 1 coverage from the Peace region
Identical Linear Regression Analysis on 36M+ Observations
Claude
Anthropic
ChatGPT
OpenAI
Gemini
Google
Julius AI
☑️ Mathematically Equivalent Results
All four platforms produced matching core statistical values
Key Finding
Analysis is independent of the Al platform used
Manual Verification
Hand calculations on sample data confirmed
Al-generated results
Cross-platform validation ensures scientific reproducibility and transparency
Novel Contribution: This project demonstrates for the first time that Canada's existing NAPS monitoring network can be repurposed as a predictive early warning system for wildfire smoke, requiring no new infrastructure, only data integration.
Proven Reliability: Historical validation across 21 years achieved 97.9% detection accuracy with zero false alarms, providing 6–48 hours of advance warning for major Canadian cities.
Actionable Results: The C.L.E.A.R. system could give schools, hospitals, and municipalities critical lead time to protect vulnerable populations before hazardous smoke arrives.
Scalable Solution: This methodology can be applied to any city with sufficient surrounding monitoring stations, making it adaptable across Canada and internationally.
Climate Urgency: With wildfire activity projected to increase, early warning systems are no longer optional—they are essential public health infrastructure.
The World Health Organization PM2.5
Air Quality Guidelines (AQGs):
Annual: 5 ug/m3
24-hour: 15 ug/m3
Date | Station | Distance | PM2.5 Reading | Threshold | Alert Triggered
June 3 | Parry Sound | 187 km NNW | 196 µg/m3 | > 139.3 µg/m3 | Emergency
June 6 | Cornwall | 387 km ENE | 160 µg/m3 | > 99.3 µg/m3 | Alert
June 6 | Toronto | - | 97 µg/m3 | (Actual) | Alert
Toronto schools could have had 3 days to cancel outdoor activities before air quality reached hazardous levels on June 6, 2023.
Wildfire smoke over the Toronto skyline, June 6, 2023.
Zou Zheng/Xinhua via Newscom.
Our system could have provided a 6- 48 hours warning before this happened.
Image 1: Wildfire smoke over the Toronto skyline, June 6, 2023. CLEAR could have provided 3 days' advanced warning. Photograph by Zou Zheng/Xinhua via Newscom.
Figure 6: Vancouver C.L.E.A.R. system. Image by Claude AI.
Figure 7: Edmonton C.L.E.A.R. system. Image by Claude AI.
Figure 5: Vancouver C.L.E.A.R. system. Image by Claude AI.
Figure 8: Montreal C.L.E.A.R. system. Image by Claude AI.